## Slide 1: Overview and a little history ofLAPPD
Thanks to everybody!
HJF
Dec 8,2011

## Slide 2: Outline
A little history- some old slides (shows how far we’ve come)
The Power of Correlated Time/Space Points
Enabling Technologies: ALD-glass MCP’s, Transmission Lines & Waveform Sampling, Surface science , Glass techniques (Joe), Material science, Simulation and analysis
The 4 Determinants of Time Resolution
  Signal/Noise (S/N)
  Analog Band-width (ABW)
  Sampling Rate
  Signal statistics
What is the ultimate resolution at a given area & cost (frugal)?
Where we can go: Water Cherenkov Counters; PET Cameras; TOF at Colliders; TOF for Fixed Target; Security; and New Ideas
Challenges- Cost, Schedule, Commercialization

## Slide 3: Our Situation Pre-LAPPD
Packaging- had 2”-square ceramic Planacon
Substrates- options: standard Pb-glass, AAO, B33/B270 Glass- many questions
Electronics- Superfast IBM-8RF bi-CMOS; expensive anodes, no back-end, no $$
Coatings- no measurements of our own- many question as to best materials
Simulation – very little understanding of MCP
Funding, personnel, home, etc.- pretty minimal

## Slide 4: Some Old Slides for fun
Feb 08, mostly…

## Slide 5
Now with Karen Byrum (physicist) and Gary Drake (Elec. Engineer) of Argonne National Lab, and Prof.’s Chin-Tu Chen and Chien-Minh Kao of the Dept of Radiology, Univ. of Chicago. Also have a MOU in progress with Saclay in France, and a close working relationship to Jerry Va’vra at SLAC. Have developed a community (e.g. Saclay workshop)
From 2005 slide

## Slide 6: The Future of Psec Timing-
From the work of the Nagoya Group, Jerry Va’vra, and ourselves it looks that the psec goal is not impossible. It’s a new field, and we have made first forays, and understand some fundamentals (e.g. need no bounces and short distances), but it’s entirely possible, even likely, that there are still much better ideas out there.
Big Questions:
What determines the ultimate limits?
Are there other techniques? (e.g. all Silicon)?
Old slide

## Slide 7: Design Goals
Colliders: ~ 1 psec resolution, < 100K$/m2
Neutrino H2O: ~100 psec resolution, < 1K$/m2
PET: ~ 30 psec resolution, < 20% of crystal cost
Micro-photograph of Burle 25 micron tube- Greg Sellberg (Fermilab)- ~2M$/m2- not including readout

## Slide 8: Characteristics we need
Feature size <~ 300 microns (= 1 psec at c)
Homogeneity (ability to make uniform large-area- think amorphous semicndtr solar-panel)
Fast rise-time and/or constant signal shape
Lifetime/robustness/simplicity
Cost/unit-area << that for photo-multipliers
Note to Howard- you were/are right!

## Slide 9: Large-area Micro-Channel Plate Panel “Cartoon”
Front Window and Radiator
Photocathode
Pump Gap
High Emissivity Material
Low Emissivity Material
`Normal’ MCP pore material
Gold Anode
50 Ohm Transmission Line
Rogers PC Card
Capacitive Pickup to Sampling Readout
N.B.- this is a `cartoon’- working on workable designs-join us…

## Slide 10: Front-end Electronics
We had started with very fast BiCMOS designs- IBM 8HP-Tang designed two (really pretty) chips
Realized that they are too power-hungry and too ‘boutique’ for large-scale applications
Have been taught by Gary Varner, Stefan Ritt, Eric DeLanges, and Dominique Breton that there’s a more clever and elegant way- straight CMOS – sampling onto an array of capacitors
Have formed a collaboration to do this- have all the expert groups involved (formal with Hawaii and France)- see talks by Tang and Jean-Francois at Lyon
Critical path item- probably the reason psec detectors haven’t been developed

## Slide 11: Get position AND time Anode Design and Simulation(Fukun Tang)
Transmission Line- readout both ends=> pos and time
Cover large areas with much reduced channel account.

## Slide 12: Photonis Planicon on Transmission Line Board
Couple 1024 pads to strip-lines with silver-loaded epoxy (Greg Sellberg, Fermilab).

## Slide 13: End Old Slides – back to the present

## Slide 14: The Large-Area Psec Photo-Detector Collaboration

## Slide 15: Time and Space Points
Pulses from the 2 ends of an 8” silk-screened cheap-glass anode strip
5 nsec/div
50 psec/pt
Matt, Bernhard, Rob; Sasha,Razib, Andrei

## Slide 16: Reconstructing the vertex space point: Simplest case- 2 hits (x,y) at wall
T1, X1, Y1
T2, X2, Y2
Vertex (e.g. p0->gg)
Tv, Xv, Yv, Zv
Photon 1
Photon 2
Detector Plane
One can reconstruct the vertex from the times and positions- 3D reconstruction

## Slide 17: The 4 Determinants of Time Resolution
  Signal/Noise (S/N)
  Analog Band-width (ABW)
  Sampling Rate
  Signal statistics
J.F. Genat, F. Tang, H. Frisch, and G. Varner; Picosecond Resolution Timing Measurements, Nucl. Instr. Meth A607, 387 (2009);
Workshop on The Factors that Limit Time Resolution in Photo-detectors, University of Chicago, April 28-29, 2011
5 nsec/div
50 psec/pt

## Slide 18: Simulation of Resolution vs abw
Jean-Francois Genat
Brown line: 10 Gs/sec (we’ve done >15);
1.5 GHz abw ( we’ve done 1.6); S/N 120 (N=0.75mv, S is app specific)
This (brown) line
This (brown) line
1 ps

## Slide 19: Can we go deep sub-picosec?: the Ritt Parameterization (agrees with JF MC)
S/N, fZ: DONE
abw: NOT YET
100 femtosec
Stefan Ritt slide, doctored

## Slide 20: Parallel Efforts on Specific Applications
.
LAPD Detector Development
PET
(UC/BSD, UCB, Lyon)
Collider
(UC, ANL,Saclay.
Mass Spec
Andy Davis, Mike Pellin, Eric Oberla
Non-proliferation
LLNL,ANL,UC
Drawing Not To Scale (!)
ANL,Arradiance,Chicago,Fermilab, Hawaii,Muons,Inc,SLAC,SSL/UCB, UIUC, Wash. U
Explicit strategy for staying on task-
Multiple parallel cooperative efforts
All these need work- naturally tend to lag the reality of the detector development
Neutrinos
(Matt, Mayly, Bob, John, ..; Zelimir)
Muon Cooling
Muons,Inc
(SBIR)
K->pnn
JPARC

## Slide 21: Neutrino Physics
Spec: signal single photon, 100 ps time, 1 cm space, low cost/m2 (5-10K$/m2)*
(Howard Nicholson)

## Slide 22: Daniel Boone
Proposal (LDRD) to build a little proto-type to test photon-TPC ideas and as a simulation testbed
`Book-on-end’ geometry- long, higher than wide
Close to 100% coverage so bigger Fid/Tot volume
Dx, Dy << 1 cm
Dt < 100 psec
Magnetic field in volume
Idea: to reconstruct vertices, tracks, events as in a TPC (or, as in LiA).
n
2 m
2 m
1 m
caps

## Slide 23: Can we build a photon TPC?
Work of Matt Wetstein (Argonne,&Chicago) in his spare time (sic)

## Slide 24: Application to Colliders
At colliders we measure the 3-momenta of hadrons, but can’t follow the flavor-flow of quarks, the primary objects that are colliding. 2-orders-of-magnitude in time resolution would all us to measure ALL the information=>greatly enhanced discovery potential.
t-tbar -> W+bW-bbar-> e+ nu+c+sbar+b+bbar
Specs:
Signal: 50-10,000 photons
Space resolution: 1 mm
Time resolution 1 psec
Cost: <100K$/m2:
A top candidate event from CDF- has top, antitop, each decaying into a W-boson and a b or antib. Goal- identify the quarks that make the jets.

## Slide 25: Colliders: Differential TOF
Rather than use the Start time of the collision, measure the difference in arrival times at the beta=c particles (photons, electrons and identified muons) and the hadrons, which arrive a few psec later.

## Slide 26: Medical Imaging (PET)
Depth in crystal by time-difference
Heejong Kim
Can we solve the depth-of-interaction problem and also use cheaper faster radiators?
Alternating radiator and cheap 30-50 psec planar mcp-pmt’s on each side
Depth in crystal by energy- asymmetry
Simulations by Heejong Kim (Chicago)
Heejong Kim

## Slide 27: Sampling calorimeters based on thin cheap photodetectors with correlated time and space waveform sampling
Proposal: Alternating radiator and cheap 30-50 psec thin planar mcp-pmt’s on each side (needs simulation work)
    Bill Moses (Lyon)

## Slide 28: Cherenkov-sensitive Sampling Quasi- Digital Calorimeters
A picture of an em shower in a cloud-chamber with ½” Pb plates (Rossi, p215- from CY Chao)
A `cartoon’ of a fixed target geometry such as for JPARC’s KL-> pizero nunubar (at UC, Yao Wah) or LHCb

## Slide 29: A `Quasi-digital’ MCP-based Calorimeter
Electron pattern (not a picture of the plate!)- SSL test, Incom substrate, Arradiance ALD. Note you can see the multi’s in both plates => ~50 micron resolution
Note- at high gain the boundaries of the multi’s go away
Idea: can one saturate pores in the the MCP plate s.t.output is proportional to number of pores. Transmission line readout gives a cheap way to sample the whole lane with pulse height and time- get energy flow.
Oswald Siegmund, Jason McPhate, Sharon Jelinsky, SSL (UCB)

## Slide 30: Challenges-

## Slide 31: Challenge 1- Making this generation of detectors
Commercial RFI for 100 tiles
(Have had one proposal for 7K- 21K tiles/yr)
Tile Development Facility at ANL
Production Facility at SSL/UCB
3 parallel paths

## Slide 32: Challenge 2- Exploiting the disruptive potential (s)
Performance:
Cost: Can we make a truly frugal tile? (what is the limit?)
(what is the
limit?)

## Slide 33: Challenge 3- the most important
People, Funding, Schedule, Satisfaction, and Fun

## Slide 34
The End

## Slide 35: Backup slides

## Slide 36: The 4 `Divisions’ of LAPPD
CV
CV
Hermetic Packaging
CV
CV
Electronics/Integration
MicroChannel Plates
Photocathodes
This talk
See (hear) Klaus Attenkofer’s talk
See (hear) Bob Wagner’s talk
See Bob Wagner’s talk

## Slide 37: The Large-Area Psec Photo-Detector Collaboration

## Slide 38: Microchannel Plates-3
SSL (Berkeley) Test/Fab Facilities
Ossy Siegmund, Jason McPhate, Sharon Jelenski, and Anton Tremsin-
Decades of experience
(some of us have decades of inexperience?)

## Slide 39: Microchannel Plates-4b
Noise (bkgd rate).
<=0.1 counts/cm2/sec; factors of few > cosmics (!)
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB
Performance:

## Slide 40: Microchannel Plates-4d
Performance: burn-in (aka `scrub’)
Measurements by
Ossy Siegmund,
Jason McPhate,
Sharon Jelinsky, SSL/UCB
Typical MCP behavior- long scrub-times
Measured ANL ALD-MCP behavior
(ALD by Anil Mane, Jeff Elam, ANL)

## Slide 41: First Pulses From an 8” MCP
Matt Wetstein, Bernhard Adams, Razib Obaid, Sasha Vostrikov (ANL and UC)
From the time difference of the 2 ends of the strip one gets the longitudinal position, from the average of the 2 ends the time (and of course from which strip(s) one gets the transverse position) => so have 2D at wall plus Time-of-Arrival
TOA (psec)
Position of laser (mm)
TrueError bar prob.
like this
(ask Matt)
Note
c= 0.3mm/ps
1/c=3.3 psec/mm

## Slide 42: Photocathodes Subject of next talk by Klaus- touch on here only briefly
LAPPD goal- 20-25% QE, 8”-square
2 parallel efforts: SSL (knows how), and ANL (learning)
ANL
Optical stand
First cathodes made at ANL
Burle commercial
equipment

## Slide 43: Photocathodes- 2 Subject of next talk by Klaus
SSL has years of experience making bialkali photocathodes-
They are our treasury bonds (Swiss francs?) in the LAPPD `portfolio of risk’

## Slide 44: `Photo-multiplier in a Pore’
Idea is to build a PMT structure inside each pore- have a defined dynode chain of rings of material with high secondary emissivity so that the start of the shower has a controlled geometry (and hence small TTS)
One problem is readout- how do you cover a large area and preserve the good timing?
Proposed solution- build anode into pores, capacitively couple into transmission lines to preserve pulse shape.

## Slide 45: The PSEC4 Waveform Sampling ASIC
PSEC4: Eric Oberla and Herve Grabas; and friends…
Eric Oberla, ANT11

## Slide 46: Good timing alone doesn’t do it-
The ALICE TPC:
Drift electrons onto wires that measure where and when for each electron.
Good time resolution would buy nothing if one integrated over a whole (blue) TPC sector- ie didn’t correlate when and where
when and where
Correlated time and space points allow 3D reconstructions

## Slide 47: Anode Testing for ABW, Crosstalk,..
Razib Obaid, Herve’ Grabas, Dave McGinnis
Crosstalk
ABW

## Slide 48: 6-channel `Scope-on-a-chip’
20 GS/scope
4-channels (142K$)
17 GS/PSEC-4 chip
6-channels ($130 ?!)
Real digitized traces from anode
Eric Oberla
(grad student)

## Slide 49: Signal- want large for S/N
We see gains > 107 in a chevron-pair
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB
ALD by Anil Mane and Jeff Elam, ANL

## Slide 50: Hermetic Packaging
Top Seal and Photocathode- this year’s priority
Commercial RFI for 100 tiles
(Have had one proposal for 7K- 21K tiles/yr)
Tile Development Facility at ANL
Production Facility at SSL/UCB
3 parallel paths

## Slide 51: Microchannel Plates
Argonne ALD and test Facilities
In situ measurements of R (Anil)
Femto-second laser time/position measurements (Matt, Bernhard, Razib, Sasha)
33 mm development program
8” anode injection measurements
Anil Mani and Bob Wagner

## Slide 52: Microchannel Plates-SSL
SSL (Berkeley) Test/Fab Facilities
Ossy Siegmund, Jason McPhate, Sharon Jelenski, and Anton Tremsin-
Decades of experience
(some of us have decades of inexperience?)

## Slide 53: Microchannel Plates
Performance: First, the gain. We see gains > 107 in a chevron-pair;
> 105 in a single plate (attractive possibility for cost/simplicity)
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB

## Slide 54: Microchannel Plates
Performance: burn-in (aka `scrub’)
Measurements by
Ossy Siegmund,
Jason McPhate,
Sharon Jelinsky, SSL/UCB
Typical MCP behavior- long scrub-times
Measured ANL ALD-MCP behavior
(ALD by Anil Mane, Jeff Elam, ANL)

## Slide 55: First Pulses From an 8” MCP (!)
Matt Wetstein, Bernhard Adams, Razib Obaid, Sasha Vostrikov (ANL and UC)
Pulses from the 2 ends of an 8” anode strip
Caveats- this is the first time…
TDIITDs- don’t over analyze this

## Slide 56: Photocathodes
LAPPD goal- 20-25% QE, 8”-square
2 parallel efforts: SSL (knows how), and ANL (learning)
ANL
Optical stand
First cathodes made at ANL
Burle commercial
equipment

## Slide 57: Photocathodes- 2
SSL has years of experience making bialkali photocathodes-
They are our treasury bonds (Swiss francs?) in the LAPPD `portfolio of risk’

## Slide 58: Hermetic Packaging
Bottom seal by Joe Gregar, ANL master glass-blower with help from Michael Minot (Minotech, Incom) and Ferro Corp
We have solved sealing over the anode strips

## Slide 59: MCP+Transmission Lines Sampled at Both Ends Provide Time and 2D Space
8” Tiles
10-15 GS/sec Waveform Sampling ASICS
Field Programable Gate Arrays
(not as shown- PC cards will be folded behind the panel- not this ugly…
Single serial Gbit connection will come out of panel with time and positions from center of back of panel

## Slide 60: 2003- Aspen Exptl Summary Talk
Invitation from Joe Lykken and Maria Spiropulu- led to psec TOF