10-20 GS/s  Sampling chip

-1   Minimum specifications.

Sampling rate              10GS/s

Analog Bandwidth      2GHz

Dynamic range            0.7V

Sampling window       adjustable 500ps-2ns

Sampling jitter            10ps

Maximum latency       TBD

Crosstalk                     1%

DC Input impedance   50 internal

Conversion clock        Adjustable 1-2 GHz internal ring oscillator. Minimum conversion time 2us.

Read clock                  40 MHz.  Readout time  (4-channel) 4 x 256 x 25ns=25.6 s

Power                          40mW/channel

Power supply              1.2V

Process                        IBM 8RF-DM (130nm CMOS)

-2   I/Os

Signal Name	Type     I/O Pad	Function

Sampling cells

Biasl_0-3		y		  Input return left

In_0-3		aI	y		  Analog inputs   0-0.7V, 50 to returns Biasl_0_3, Biasr_0_3

Biasr_0-3                     y                       Input return right

Write_0-255    dI         n                       Store voltages across the sampling cells (timing).

Ctrl_rd_0-4     dI         y                       Read switch control. Enables the sampling cell voltage onto the

ADC’s comparator

Vpol_cell         aI         y                       Bias current sampling cell  (vpol)

Trig_0-4          dI         y                       Sample and Hold   (trig)

High: sample, Enables the sampling windows closing the sampling switches.

Low:  hold,     Stops the recording process. All sampling switches open.

Timing generator

MCk                dI       	 y		 Write clock (40 MHz to timing generator)

MCk_ret          dI    	 y            	 Write clock return

VCN                aI          y                      Timing cell control (falling)

VCP                 aI         y                                                       (rising)

VDL_out         dO        y                       Output from VCDL for delay lock

VSw_n             aI         y                       Sampling window control (rising edge)

VSw_p             aI         y                       Sampling window control (falling edge)

Out_0-255                    n                       Sampling windows to sampling cells

7

ADC control

Cext		aIO	y		  External ramp input or internal ramp output (Vrampout)

Ibias _rp          aI         y                        Ramp current

Ibias_buf         aI         y                        Ramp analog buffer (one for each channel)

Rp                   dI         y                        Ramp (Ramp) active low, 	High clears the ramp cap.

Rp_ret                         y                        Rp return

V2GN              aI	y		  Controls 2G counter ring oscillator (falling)

V2GP               aI        y                                                                                  (rising)

Ck_cv      	dO	y	              Buffered ADC clock output monitors (2 GHz/4096=500 kHz).

Clear_ADC     dI         y                        Clears the ADC counter before conversion.

Ibias_comp      aI         y                        Comparator’s biasing

10

Read control

Ck_rd   	 dI         y                       Read clock (40 MHz)

Ck_rd_ret                     y                       Read clock return

Tok_in             dI         y                        Input of the token passing

Tok out            dO        y                       Output of the token passing

Clear_token      dI        y                        Clear token

AD0-4              dI	 y		   Channel address,  Selects channel to be read.

D0-11		 d I	 y                        12-bit data bus controlled by the token and AD0_4. Tied to Gnd

in the Hi-Z state with a large internal resistor.

22

Power supplies

Vdd				12	+1.2V

Gnd                             		28         0V

Test structures

Sampling cell

Biasl_test      aI    y		      Input return

In_test	          aI    y		      Analog input    .7-0V

Vpol_cell      aI    y                       Bias sampling cell

Trig_test       dI    y		      Sample and Hold

Write_test     dI    y                       Write_test

Samp_out     dO   y                       Sampling cell out (after buffer)

Ctrl_rd_test  dI    y                        Read sampling cell

7

Comparator

Comp_n        aI    y		       Test comparator input -

Comp_p        aI    y 		       Test comparator input +

Comp_out     aO   y		       Test comparator output

3

Ring Oscillator

Clear_test         y		       Clears the test RO counter

2G_test_out      y                           500 kHz output after 2G division by 4096

2

Chip:

74 I/Os

40 Gnd

30 Vdd

144 pads

Package CQFP120A:

74 I/Os

34 Gnd

12 Vdd

120  pads

All analog inputs protected with DC path to Gnd and Vdd +/- .6V   (5 x 10 m2 diodes).

-3     Operation Modes

Modes   		Write		Writes continuously samples of inputs in a caps arrays at 10 GS/s for 25.6s.

Sampling stopped upon trigger.

Convert           Clears 2 GHz counter, ramp up Wilkinsons for 2 s.

Read                Sequences 256 counters of the channel selected by AD1-5 onto the data bus

at 40 MHz read clock rate.

-4     Layout

Blocks sizes:    Timing generator  		10 x 10    m2		x 256

Sampling cell        		10 x 25		“

Comparator            		10 x 30		“

Counter                 		10 x 300		“

Token                    		10 x 40		“

Ramp                      		100 x 300

Ramp buffer			260 x 65

Ring Oscillator 	 	10 x 50

Divider			10 x 300

Size: 4000x 4000 m2

-5   Tests

-1 DC Tests.    Goals: Measure Vdd current vs biasing voltage for all test blocks. Disable, enable blocks one by one.

Compare with simulations.

Test card:  use packaged chips and DC inputs, some LEMOs to check the test structures.

-2 AC Tests.   Goals:  Measure the AC performance of  the test structures. RO frequency vs voltage, comparator’s time response vs threshold, sampling cell output vs input and (external) sampling window, full functionality (see below).

Test card: use bare dies wire bonded straight on PCB.  FPGA for control and readout from/to a VME interface.

- Observe the sampling window in channel 5.

- Input a fast rising edge. Observe output rise-time vs sampling rate, internal sampling window’s width.

- Maximum sampling frequency.

- Linearity/dynamic range.

- Measure output noise with grounded inputs.

- Voltage supply range.

# Text boxes

Ck_rd

Token

Ramp

Buffer

260x65

Ramp

Buffer

260x65

Ramp

Buffer

260x65

Ramp

Buffer

260x65

RO

350 x 10

Tests structures

Sampling cell

10 x 40

Comparator

30 x 10

Comp test

SCA Channel 4    2560 x 400

ADC’s

SCA Channel 2    2560 x 400

ADC’s

SCA Channel 1    2560 x 400

ADC’s

SCA Channel 0    2560 x 400

ADCs

2560 x 400

Timing Generator 2560 x 10

Ramp

300 x 100

Trig 0-3

Ctrl_rd 0-3

AD 0-4

RO controls

ADC ck

Data

Write ck     Delays  ctrl        Sampling window control                                                           ADC controls

Sampling cell test                     Data

Inputs 0-3

RO_test

Data out

RO

350 x 10

Token                  2560 x 40

Sampling Array

SCA Channel 3    2560 x 400

ADC’s